## Slide 1: SCION Implementation

## Slide 2: SCION Architecture Overview
Source
Destination
PCB
PCB
PCB
PCB
Trust domain (TD)s
  Isolation and scalability
Path construction
  Path Construction Beacon (PCB)
Path resolution
  Control
  Explicit trust
Route joining (shortcuts)
  Efficiency, flexibility
S: blue paths
D: red paths
path srv
TD
TD Core
AD: admin domain
Notes: Al the nodes shown in this figure represent a TD, e.g., united states
Each node can be though of as an ISP or administrative domain, or AD
Path construction achieves scalability
Path resolution achieves control

## Slide 3
C
TD 4
Core
TD2
Core
TD1 Core
P
B
P
B
TD1 Core
TD 3
Core
Peer
Trust Domain Boundary
C
P
P
P
TD Core AD
AD
C : Certificate Server
B : Beacon Server
P : Path Server
Router
TD Core Interconnect
B
SCION Trust Model

## Slide 4
TDCore
Transit AD
Endpoint AD
Path Server
Beacon Server
Certificate Server
Policy File
Topology File
Certificates
Topology File
Entity List
  1. Certificate Server : CS
  2. Beacon Server : BC
  3. Path Server : PS
  4. Gateway : GW
  5. Border Router : BR
Neighbor List -> Why necessary?
BS, CS need this
Registered Paths
Database
Key Table
(Op gen keys/
Public Keys)
Update to all
+ DNS

## Slide 5
TDCore
Transit AD
Endpoint AD
Path Server
Beacon Server
Certificate Server
Policy Update
Topology Update/Distribution
Cert. Issue/ Update Distribution
Path Registration/ Resolution
Services
Beacon Generation
Key Management
Offline
Offline

## Slide 6
Transit AD
Path Server
Beacon Server
Certificate Server
Server List
Server List
Topology File
Certificates
All path to/from TDCore
Cache paths to other Endpoint ADs
Database
Update topology file & entity status check
Distribute topology file
Key Table
Path Disclosure Policy Configuration Table
(Ingress to Egress mapping,
# of Paths to propagate)
Key Server

## Slide 7
Transit AD
Path Server
Beacon Server
Certificate Server
Server List
Server List
Topology Update/Distribution
Certificate Management
(Fetch from Provider/ Distribution to Customer)
Path Resolution service
Services
Beacon Propagation
Key Management
K path selection/registration
Path distribution to Path Server(s)
Key Server

## Slide 8
Transit AD
Server List
Certificates
Path Server
Beacon Server
Certificate Server
paths to TDC
Intra-TD Messages
Certificates
Key distribution
Path Query from End host

## Slide 9
Transit AD
Path Server
Beacon Server
Certificate Server
PCB
Path Query from End host
Inter-TD Messages
Certificate Queries

## Slide 10
P
B
C
❶ Topology distribution (broadcast)
❷
❷ master OFG key distribution (to B and border routers)
❸
❸ AD public key Request/Reply
Certificate Server Messages
❶
C
C : Certificate Server
B : Beacon Server
P : Path Server
Border Router
❸

## Slide 11
P
B
C
❶
❶
❶
❶
❶ PCB propagation
❶
❶
❷
❷ Path distribution
❸
❹ AD public key request/reply
❺ master OFG key request/reply (bootstrap)
❹
Beacon Server Messages
❺
❸ Path registration (to TDC)
C : Certificate Server
B : Beacon Server
P : Path Server
Border Router

## Slide 12
P
B
C
❶ Path query (k registered paths, bootstrap)
❷
❷ Certificate request/reply (internal entities)
❸
❸ Path query (form endhosts)
Path Server Messages
❶
P
P
❶
❶
C : Certificate Server
B : Beacon Server
P : Path Server
Border Router
❹ Path query (to TDC path server)
❹

## Slide 13: Root Of Trust File
<ROT>
<header>
<policyNumber> “Policy Number” </policyNumber>
<TDID> “Trust Domain ID” </TDID>
<policyThreshold> “Policy Threshold” </policyThreshold>
<certificateThreshold> “Certificate Threshold” </certificateThreshold>
</header>
<coreADs>
<coreAD>
<AID>”AID”</AID>
<publicKey>”Public Key”</publicKey>
</coreAD>
:
:
<coreAD>
<AID>”AID”</AID>
<publicKey>”Public Key”</publicKey>
</coreAD>
</coreADs>
<signatures>
<coreAD>
<AID>”AID”</AID>
<sign>”Signature”</ sign>
</coreAD>
:
:
<coreAD>
<AID>”AID”</AID>
<sign>”Signature”</sign>
</coreAD>
</signatures>
</ROT>

## Slide 14: Topology File
<TDID> “TD ID” </TDID>
<ADID> “AD ID” </ADID>
<Topology>
<Servers>
<BeaconServer> “AID” </BeaconServer>
<PathServer> “AID” </PathServer>
<CertificateServer> “AID” </CertificateServer>
</Servers>
<BorderRouters>
<Router>
<AID>”AID”</AID>
<Interface>
<IFID>”Interface ID”</IFID>
<NeighborAD>”AD ID”</NeighborAD>
<NeighborType>”Neighbor Type”</NeighborType>
</Interface>
<Interface>
<IFID>”Interface ID”</IFID>
<NeighborAD>”AD ID”</NeighborAD>
<NeighborType>”Neighbor Type”</NeighborType>
</Interface>
:
</Router>
:
:
</BorderRouters>
<Gateways>
<Gateway>
<AID>”AID”</AID>
<Protocol>”Protocol Type”</Protocol>
</Gateway>
:
:
</Gateways>
</Topology>
<Signature> “Signature” </Signature>

## Slide 15
Path Server
Registered Paths
Path Server
Key: Endpoint AID, Value: PCB Header
Path Registration/Request
Maintain (Key, (Type, Value)) database (file or RDB?)
Key: AD AID
Type: Public/Private(encrypted)/Internal(within TD)/External(outside TD)
* Need to define Types
Value: List of Paths (from TDC to AID)
where a Path is timestamp||EXP||Hops||OFs||OF in PCB Header (viz., Header)
Counter: # of registrations / day (limited by MAX), Q: day or hour?
A Key has k Values – implement using HashMap with value as a List
Path Registration
Request: Type – PATH_REG_REQ, Args - AID, Type, PCB Header, Signature
Reply: Type – PATH_REG_REP, Ret - Success/Fail, Fail should contain “Error Code”
* new registration automatically replaces the oldest entry
Path Request
Request: Type – PATH_REQ, Args - TID(sender), AID(sender),TID(receiver), AID(receiver), Type
Reply: Type – PATH_REP, Ret - AID, PCB Header (i.e., a series of (AID, Opaque Field))

## Slide 16
Beacon Server
Beacon Server
Key Table
(Op gen keys/
Public Keys)
Key: Timestamp, Value: Opaque Field Generation Key
PCB Propagation
Maintain most recent (Timestamp, master Opaque Field Generation Key) acquired
from Certificate Server (CS)
Request the pair to CS if it does not have (e.g., due to reboot)
How often should the OFG Key renew?
Maintain (AID, Public-Key) for PCB signature verification
Request the pair to CS if it does not have (first seen AID)
Start Queueing PCBs if a new timestamp arrives – use per child AD queue / verify sign. on arrival
Stop Queueing PCBs if current_time – start_time(of current timestamp) > MAX_PROP_DELAY
Pick k PCBs per child AD based on the preset rules;
0. local policy (traffic engineering)
1. shortest path length
2. maximally disjoint from previous n propagation
3. ?
Mark Opaque Field with the present OFG key; H(master OFG key||timestamp)
Propagate k PCBs to children and purge Queue
Add the present OFG key to Key Table (index, the present OFG key)
Multicast all (or selected) Paths to local Path Servers after removing all signatures and adding its own signature (use for best effort paths)

## Slide 17
Beacon Server
Beacon Server (cont.)
Key Table
(Op gen keys/
Public Keys)
Key: Timestamp, Value: Opaque Field Generation Key
k path (TDCore to itself) selection / registration
Pick a PCBs per child AD based on the preset rules;
0. local policy (e.g., preferred path, price)
1. shortest path length
2. maximally disjoint from previous n propagation
3. ?
Register the path to TDCore
Multicast the path to local Path Servers
Repeat until k paths are chosen
Renew a path for the following cases
1. a registered path expires
2. a better path arrives
3. a registered path is under attack
4. explicit request from customers
How to set k? k=10 / provider, how many k’ (private paths)?

## Slide 18
Certificate Server
Topology File
Certificate Server
Server List
Maintain Server List
HashMap of (Type, AID) pair
1. Main Certificate Server, Endpoint AID
2. Main Beacon Server, Endpoint AID
3. Main Path Server, Endpoint AID
* Note: Main Servers redirect requests to distributed servers
Path Servers may use DHT.
Broadcast “Server List” to all entities inside the AD by signing it (whenever updated)
- Type: BCAST_SVR_LIST, dest AID: 0xFFFFFFFF (have to define BCAST address)
An entity pulls “Server List” on bootup using anycast
- Anyone who receives the request replies
- Type: REQ_SVR_LIST, dest AID: 0xFFFFFFFE (have to define ACAST address)
Entity List
Maintain Entity List (XML?)
HashMap of (AID, Property)
Property: (Type, Mac Addr, Certificate, Interfaces)
- Type: Border Router, Server, Gateway, …
- Interfaces: (Interface ID, Neighbor ID);
Neighbor ID = AD ID for Border routers, interface ID for internal interface

## Slide 19
Certificate Server
Certificates
Certificate Server
Certificate List
Maintain two Certificate Lists
AD certificate – PCB verification
Entity certificate – local entities
Certificate Request
Local: Type – INT_CERT_REQ, Dest AID - Addr of Certificate Server
Inter-AD: Type – EXT_CERT_REQ, Dest AID – 0xFFFFFFFE (Ingress router writes the AID of CS)
Data: Count (# of certificates requested), List of (TID, AD ID)
Certificate Reply
Local: Type - INT_CERT_REP
Inter-AD: Type – EXT_CERT_REP, Dest AID – 0xFFFFFFFE (Ingress router writes the AID of CS)
Data: TID, AD ID, Certificate
* Note: reply one certificate at a time (Certificate size is ~ 1KB)
upstream AD should have the requested certificate unless it recovered from failure

## Slide 20
Certificate Server
Certificate Server
Key Server collocated in Certificate Server
Offline Key (KAD)
Online Key (KOp)
Symmetric Key of AD
Master Opaque Field Generation Key
Offline Key
Symmetric Key for internal message encryption
Preinstalled to individual entities
Online Key
Certificate Server generates master Opaque Field Generation Key (KOp) periodically (e.g., once a day)
Multicast the key (KOp) to Boarder Routers (for Opaque Field verification)
Type: INT_KEY_OFG_MCAST
Data: Enc(CurrentTime||StartTime||Endtime||Kop)||MAC;
Border Router, on its startup, requests the key (KOp) directly to the CS (or any Border Router nearby).
Type: INT_KEY_OFG_REQ / INT_KEY_OFG_REP

## Slide 21
Certificate Server
Policy File
Certificate Server
Policy
Describe how many AD agree on a specific policy
Policy number
TD ID
# of ADs that need to sign to generate a new policy
Need to decide
how the Policy Number would be used
who needs the Policy File
the contents that the Policy File contains
Do we need a threshold signature scheme for a Policy File update? (probably no…)

## Slide 22
Click Router
Kernel Mode
User Mode
Click Modular Router
- No need for ethernet frame handling
- Flexible to be implemented as a SCION routers,
switch, servers
- Create many instances in a system
-> configure a system as an AD
Todo
Switch implementation
Communication protocols between entities
Broadcast within an AD?
Header format
Data format
Internal forwarding mechanism

## Slide 23
Click
CS
Click
PS
Click
BR
Click
BR
Click
BR
Click
BR
Transit AD
Click
PS
Configuration
Single Machine
SCION
Switch
Click
BS
Click
PS
Click
…
Click Instance

## Slide 24
Click
CS
Click
PS
Click
PS
Transit AD
Click
BR
Click
BR
Click
BR
Click
BR
Click
PS
Configuration
Single Machine
SCION
Switch
Click
BS
Click
…
VM

## Slide 25
Configuration
STUB2
Single Machine
SCION
Switch
Click
Switch as
Virtual NIC
SCION
Switch
STUB1
STUBn
AD1
Single Machine
SCION
Switch
Core
AD2
Physical Link
/ 2
/
2
/ 2
/ 2
/ 3
/ 3

## Slide 26: SCION Switch using VNIC
Switch Function
  Click entities send/receive packets through SCION Switch
  SCION Switch forwards packets to NIC if a destination is outside the physical machine
Configuration
  Router interface: RID-IID
    RID: Router ID
    IID: Interface ID
    SID: Switch ID
  Internal: RID-IID –> SID –> RID-IID
  External (outgoing): RID-IID –> SID –> NIC
  External (incoming): NIC –> SID –> RID-IID
  External requires composition of outgoing and incoming
Switch needs to know
  Whether RID belong to internal or external
  Which NIC to forward a packet (if a machine has multiple NICs)

## Slide 27: SCION Switch
Has the configuration information
  List of RIDs within a local machine
  List of RIDs that belong to external entities
  If external, which NIC needs to be used for forwarding

## Slide 28: Questions
K path propagation from BS -> limited path diversity at downstream
PCB propagation to BS -> Cert. Server should have all AD certificates on the paths (too many certs at Stub ADs)
PBC verification at BS -> MAC verification on Opaque Fields in Data Packets? (Edge routers verifies opaque fields)

## Slide 29: Need to be decided
How to efficiently manage Path Servers at the TDC; e.g., using DHT…
How to manage Certificate Server at the TDC; Should the Cert. issue/rev protocol be online?; Why should we use quorum based protocol?
What’s the specific role of policies?
Path server management at endpoint/transit ADs; most likely pull based, yet how often and how many to cache?

## Slide 30
SCION Packet Format
0-7 | 8-15 | 16-23 | 24-31 | 32-39 | 40-47 | 48-55 | 56-63
Type ¦ Class |  | Total Length |  | Frag ID |  | Frag Offset | 
Source AID |  |  |  |  |  |  | 
Destination AID |  |  |  |  |  |  | 
Timestamp[0] |  |  |  | Timestamp[1] |  |  | 
Hops | OFs | XOVR | LHops | Current IF |  | VerROT | 
PAYLOAD |  |  |  |  |  |  | 
SCION Header
Header Info
Path Header
Bit Offset
Endpoints
Type: BEACON, DATA, CERT_REQ, CERT_REP, PATH_REQ, PATH_REP, …
Class: Service Priority
Total Length: Total Packet Length (including header)
Frag ID: ID for reassemble fragments (caused by different MTUs)
Frag Offset: Offset that the current fragments starts
Timestamp[0]: Up-path
Timestamp[1]: Down-path
Hops: Current hop in the forwarding path, LHops: Total # of Hops from source to destination AD
OFs: Current index of Opaque Fields in the header (a single AD can add multiple OFs)
XOVR: Index of Crossover AD
Current IF: Interface ID of the current destination (used by BS to propagate PCB to egress IF)
40 Bytes

## Slide 31
SCION Packet Format
0-7 | 8-15 |  | 16-23 | 24-31 |  | 32-39 | 40-47 | 48-55 | 56-63
AD AID 1 |  |  |  |  |  |  |  |  | 
Ingress IF |  | Egress IF |  |  | EXP | LSign |  | Block Size | 
MAC |  |  |  |  |  | MAC |  |  | 
TD ID |  |  |  |  |  | Reserved |  |  | 
RSA Signature (LSign Bytes) |  |  |  |  |  |  |  |  | 
AD AID 2 |  |  |  |  |  |  |  |  | 
AD AID n |  |  |  |  |  |  |  |  | 
SCION Payload (PCB)
AD [1]
AD [2]
AD [n]
Opaque Field
Signature
AD AID: authenticated ID of AD; e.g., ASN; if Egress IF is 0, this field indicates peer AD
Ingress IF (15bits): ingress interface id (internal use)
Egress IF (15bits): egress interface id (internal use) or egress interface id of peering link if the OF is for the peering link (for peering link, Egress IF is same as that of previous OF because they are marked by the same AD)
EXP: lifetime, current assignment: 0x00-6HR, 0x01-12HR, 0x02-18HR, 0x03-24HR
LSign: Signature length (e.g., 1024 bits, 2048 bits)
Block Size: total marking block size of AD[i], which includes all peering links
MAC: Massage Authentication Code, MAC(i) = HKi(Ingress IF||Egress IF||OF(i-1)||AIDi+1)
H() – SHA1 Hash, Ki – MAC generation key of AD[i]
TD ID: Trusted Domain ID, only for Inter-TD peering link
Signature: RSA Signature signed by AD[i]

## Slide 32
SCION Packet Format
0-7 | 8-15 |  | 16-23 | 24-31 |  | 32-39 | 40-47 | 48-55 | 56-63
Ingress IF |  | Egress IF |  |  | EXP | MAC |  |  | 
MAC |  |  |  |  |  | CAP |  |  | 
Ingress IF |  | Egress IF |  |  | EXP | MAC |  |  | 
MAC |  |  |  |  |  | CAP |  |  | 
Ingress IF |  | Egress IF |  |  | EXP | MAC |  |  | 
MAC |  |  |  |  |  | CAP |  |  | 
Payload |  |  |  |  |  |  |  |  | 
SCION Payload (Data)
Capability [1]
Opaque Field[1]
Ingress IF: ingress interface id (internal use)
Egress IF: egress interface id (internal use)
MAC: Massage Authentication Code, MAC(i) = HKi(Ingress IF||Egress IF||OF(i-1)||AIDi+1)
H() – SHA1 Hash, Ki – MAC generation key of AD[i]
CAP: Capability, CAP(i) = HKi(source AID||destination AID||Ingress IF||Egress IF)
Reserved: bandwidth class, expiration time, and so on
Payload: higher-layer header and data
16 x MAX_HOPS Bytes
Capability [2]
Opaque Field[2]
Capability [n]
Opaque Field[n]

## Slide 33
SCION Packet Construction /Forwarding (TYPICAL)
TDC’ | OP11 | OP22 | OP33
OP03 | OP02 | OP01 | TDC | TDC’ | OP11 | OP22 | OP33
OP03 | OP02 | OP01 | TDC
Up-path
Down-path
Hops | OFs | XOVR
1 | 1 | 4
Hops | OFs | XOVR
2 | 2 | 4
+
Hops | OFs | XOVR
8 | 8 | 4
Hops | OFs | XOVR
7 | 7 | 4
❶
❷
❽
❼
❶
❷
❼
❽
PCB propagation

## Slide 34
SCION Packet Construction /Forwarding (CROSSOVER)
TDC’ | OP01’ | OP12 | OP13
OP03 | OP02 | OP01 | TDC | TDC’ | OP01’ | OP12 | OP13
OP03 | OP02 | OP01 | TDC
Up-path
Down-path
Hops | OFs | XOVR
1 | 1 | 3
Hops | OFs | XOVR
2 | 2 | 3
+
Hops | OFs | XOVR
6 | 6 | 3
Hops | OFs | XOVR
5 | 5 | 3
❶
❷
❸
❶
❷
❺
❻
❹
❺
❻
❸
❹
Hops | OFs | XOVR
3 | 3 | 3
If Hops == XOVR,
Egress Router of OP01
  validates both OP01 and OP01’
  forward packet to Egress IF in OP01’
PCB propagation

## Slide 35
SCION Packet Construction /Forwarding (ON-PATH)
TDC’ | OP01’
OP03 | OP02 | OP01 | TDC | TDC’ | OP01’
OP03 | OP02 | OP01 | TDC
Up-path
Down-path
Hops | OFs | XOVR
1 | 1 | 3
Hops | OFs | XOVR
2 | 2 | 3
+
❶
❷
❸
❶
❷
❹
❸
❹
Hops | OFs | XOVR
3 | 3 | 3
If Hops == XOVR and LHops == Hops +1,
Egress Router of OP01
  validates both OP01 and OP01’
  forward packet to Destination Endpoint (i.e., AID)
PCB propagation

## Slide 36
SCION Packet Construction /Forwarding (SHORTCUT)
TDC’ | OP11 | OP01’ | OP12 | OP13
OP03 | OP02 | OP11’ | OP01 | OP11 | OP01’ | OP12 | OP13
OP03 | OP02 | OP11’ | OP01 | TDC
Up-path
Down-path
Hops | OFs | XOVR
1 | 1 | 0
Hops | OFs | XOVR
2 | 2 | 0
+
Hops | OFs | XOVR
6 | 6 | 0
Hops | OFs | XOVR
5 | 5 | 0
❶
❷
❸
❶
❷
❺
❻
❹
❺
❻
❸
Hops | OFs | XOVR
3 | 3 | 0
* OP11’ is the shortcut to OP11 marked by OP01
* OP01’ is the shortcut to OP01 marked by OP11
❹
Hops | OFs | XOVR
4 | 4 | 0
PCB propagation

## Slide 37
SCION Packet Construction /Forwarding (Inter-TD SHORTCUT)
TDC’ | OP01’ | OP12 | OP13
OP03 | OP02 | OP01 | OP01’ | OP12 | OP13
OP03 | OP02 | OP01 | TDC
Up-path
Down-path
Hops | OFs | XOVR
1 | 1 | 3
Hops | OFs | XOVR
2 | 2 | 3
+
Hops | OFs | XOVR
6 | 6 | 3
Hops | OFs | XOVR
5 | 5 | 3
❶
❷
❸
❶
❷
❺
❻
❹
❺
❻
❸
❹
Hops | OFs | XOVR
3 | 3 | 3
If Hops == XOVR,
Egress Router of OP01
  validates both OP01 and OP01’
  forward packet to Egress IF in OP01’
PCB propagation

## Slide 38: Log
Naming: ADiRj.log, ADiCS.log, ADiBS.log, ADiPS.log
  Log filename is defined in the .conf file
Format: LType, Timestamp, MType, Status, Size, Content
  Timestamp: current time (μs)
  LType (log type): Error (1~), Warning (101~), Information (201~), … Each of which has Low, Medium, High sub-types (default is M); i.e., EM (2), WM (102), IM (202)
  MType (message type): BEACON, DATA, CERT_REQ, CERT_REP, PATH_REQ, PATH_REP, … (defined in the header)
  Status: Q (queued), S (serviced), D (dropped)
  Size: packet size (including SCION header)
  Content: type specific messages
    Error; e.g., “can’t connect to CS”
    Warning; e.g., “Opaque Field verification failure”
    Information: e.g., “PCB propagates to xxx”
Logging level is defined in the .conf file and messages having LType <= LogLevel are logged at the .log file.
printLog(LType, Mtype, fmt);
Fmt optionally includes Opaque Fields (for debugging purpose) at the end. This also is defined in the .conf file.

## Slide 39: Need to be decided
How big should be the signature size? (RSA key size: 1024? 2048?)
Is MAC (in OF generation) chaining necessary?
  Gap between PCB construction and OF verification
Are we going to allow Inter-TD shortcut?
How the policy file (or a specific policy) would be used by, propagate to, and be interpreted by ADs.
Policy update: would a threshold signature scheme be used? Is signature privacy needed?